The following call message sequence diagrams show signaling messages handled by MaxBox. Solid arrows are messages that are exchanged in the bearer channel; dotted arrows are messages that are exchanged on a signaling channel.

| Phone |  | MaxBox |  | Network Call Server |
| --- | --- | --- | --- | --- |
| Offhook |  |  |  |  |
|  |  | Play dialtone |  |  |
| First digit |  |  |  |  |
|  |  | Stop the dialtone |  |  |
| Additional digits |  |  |  |  |
| End-of-dial digit |  |  |  |  |
|  |  | Digit analysis for provisioned rule |  |  |
|  |  | Establish GW resource and receive port; initiate depacketization on the receive port |  |  |
|  |  | Call setup procedure |  |  |
|  |  | Call progress tone |  |  |
|  |  |  |  | Alerting/Connect |
|  |  | Stop call progress tone. |  |  |
|  |  | Initiate packetization of the phone line activity |  |  |

Figure 1 Call originated to a Broadband Network end-point

| Phone |  | MaxBox |  | Network Call Server |
| --- | --- | --- | --- | --- |
| Offhook |  |  |  |  |
|  |  | Play dialtone |  |  |
| First digit |  |  |  |  |
|  |  | Stop the dialtone |  |  |
| Additional digits |  |  |  |  |
| End-of-dial digit |  |  |  |  |
|  |  | Digit analysis for provisioned rule |  |  |
|  |  | Establish GW resource and receive port; initiate depacketization on the receive port |  |  |
|  |  | Call setup procedure |  |  |
|  |  | Call progress tone |  |  |
|  |  |  |  | Reject with followon activity command |
|  |  | Stop call progress tone. |  |  |
|  |  | Stop depacketization and freeup GW resource |  |  |
|  |  | Initiate a call on PSTN interface in accordance with the command received from the Network server |  |  |

Figure 2 Call originated to a PSTN end-point

| Phone |  | MaxBox |  | Network Call Server |
| --- | --- | --- | --- | --- |
| Offhook |  |  |  |  |
|  |  | Play dialtone |  |  |
| First digit |  |  |  |  |
|  |  | Stop the dialtone |  |  |
| Additional digits |  |  |  |  |
| End-of-dial digit |  |  |  |  |
|  |  | Digit analysis for provisioned rule |  |  |
|  |  | Initiate a call on PSTN interface |  |  |
|  |  | Call setup procedure |  |  |

Figure 3 Call originated to a pre-provisioned number